## Slide 1: Cellular Networks: 4G (Long Term Evolution) and 5G (Fifth Generation) Course: Wireless and Mobile Communication
Md. Ashikujjaman Nur (IT-21013)
November 9, 2025
4G (Long Term Evolution) and 5G (Fifth Generation)

## Slide 2: What are Cellular Networks?
Radio-based wide-area networks that connect mobile devices to the internet and voice services.
Generations: First Generation (1G) → Second Generation (2G) → Third Generation (3G) → Fourth Generation (4G, Long Term Evolution
- LTE) → Fifth Generation (5G).
Why it matters: broadband mobility, Internet of Things (IoT), and automation.
1G
1980s
2G
1990s
3G
2000s
4G
2010s
5G
2020s
4G (Long Term Evolution) and 5G (Fifth Generation)

## Slide 3: 4G (Long Term Evolution - LTE) at a Glance
All-Internet Protocol (All-IP) network: voice and data over packet core.
Speed: approximately 100 Megabits per second (Mbps) for mobile users, up to
1 Gigabit per second (Gbps) for stationary users.
Latency: around 50 milliseconds (ms).
Key enablers: Orthogonal Frequency Division Multiple Access (OFDMA) and Multiple Input Multiple Output (MIMO).
Evolved Node B (eNodeB) (Base Station)
Internet
User Equipment (UE) (Phone)
LTE Air Interface
S1 Interface
Evolved Packet Core (EPC) Internet Protocol (IP)
4G (Long Term Evolution) and 5G (Fifth Generation)

## Slide 4: How 4G (LTE) Works
Orthogonal Frequency Division Multiple Access (OFDMA): splits spectrum into many narrow subcarriers to improve robustness and throughput.
Multiple Input Multiple Output (MIMO): uses multiple antennas for better data rates and reliability.
Architecture: User Equipment (UE) → Evolved Node B (eNodeB) → Evolved Packet Core (EPC) → Internet.
Limitations: congestion in dense areas; less optimized for massive Internet of Things (IoT) devices.
4G (Long Term Evolution) and 5G (Fifth Generation)

## Slide 5: 5G (Fifth Generation): Designed for a Connected World
Speed: up to 10 Gigabits per second (Gbps).
Latency: less than 10 milliseconds (ms) in Ultra-Reliable Low-Latency Communication (URLLC) scenarios.
Capacity: up to 100 times more connected devices per square kilometer than 4G.
Built for Enhanced Mobile Broadband (eMBB), Massive Machine-Type Communication (mMTC), and
Ultra-Reliable Low-Latency Communication (URLLC).
))
Next Generation Node B (gNodeB)
ECN
Car
IoT
VR
4G (Long Term Evolution) and 5G (Fifth Generation)

## Slide 6: 5G Key Technologies
Millimeter Wave (mmWave) Spectrum: provides ultra-high data rates but limited range.
Massive Multiple Input Multiple Output (Massive MIMO): hundreds of antennas enable narrow, efficient beams.
Network Slicing: creates multiple virtual networks for different services.
Edge Computing: processes data close to users for reduced latency.
4G (Long Term Evolution) and 5G (Fifth Generation)

## Slide 7: Applications of 4G and 5G
4G (LTE):
High-speed mobile internet, HD streaming, and Voice over LTE (VoLTE). Mobile hotspot and broadband services.
Internet of Things (IoT) using LTE-M and Narrowband IoT (NB-IoT).
5G:
Smart cities and Massive IoT (mMTC). Connected and autonomous vehicles.
Remote healthcare and telesurgery (URLLC). Augmented and Virtual Reality (AR/VR).
Industrial automation (Industry 4.0).
4G (Long Term Evolution) and 5G (Fifth Generation)

## Slide 8
Comparison Among 1G to 5G
Feature | 1G | 2G | 3G | 4G (LTE) | 5G
Era | 1980s | 1990s | 2000s | 2010s | 2020s
Technology | Analog (FDMA) | Digital (TDMA/CDMA) | WCDMA/CDMA2000 | OFDMA, MIMO | OFDMA
Speed | 2.4 kbps | 64–384 kbps | 2–30 Mbps | 100 Mbps–1 Gbps | 1–10 Gb
Latency | 500+ ms | 300 ms | 200 ms | 50 ms | <10 ms
Core Network | Circuit-switched | Circuit-switched | Packet + Circuit | All-IP (EPC) | Cloud-na
Main Service | Voice | Voice, SMS | Internet, Video | HD Streaming, VoLTE | IoT, A
4G (Long Term Evolution) and 5G (Fifth Generation)

## Slide 9: Takeaways
4G (Long Term Evolution - LTE) enabled true mobile broadband with all-IP architecture.
5G (Fifth Generation) builds on 4G by offering ultra-high speed, low latency, and massive connectivity.
Cellular networks have evolved from analog voice to a digital ecosystem enabling smart cities and industries.
“The future is wireless — and it’s already here.”
4G (Long Term Evolution) and 5G (Fifth Generation)